## Slide 1: EMBSYS 105 Programming with Embedded & Real-Time Operating Systems
Instructor: Nick Strathy, nstrathy@uw.edu
TA: Gideon Lee, gideonhlee@yahoo.com
© N. Strathy 2020
Lecture 2 1/13/2020

## Slide 2: Looking ahead
Date | Lecture number | Assignment
1/6 | L1 | A1 due* before L2
1/13 | L2 | A2 due before L3
1/20 | Holiday (?) | 
1/27 | L3 | A3 due before L4
2/3 | L4 | A4 due before L5
2/10 | L5 | A5 due before L7, Project due before L10
2/17 | Holiday (?) | 
2/24 | L6 | 
3/2 | L7 | 
3/9 | L8 | 
3/16 | L9 | 
3/23 | L10 – Student presentations | 
* Assignments are due Sunday night at 11:59 PM

## Slide 3: Next week’s holiday(?)
Whereas:
Next week is a holiday (MLK Day)
We therefore have no class scheduled
Which breaks momentum as our course is starting up
And pushes our course end-date one week later
Be it resolved:
That we hold our lecture next week, anyway
That attendance not be required (you can watch the recording later)
All those in favor: you don’t need to say a word.
All those opposed: let me know by end-of-day tomorrow

## Slide 4: Previous lecture (L1) overview
Embedded Operating System Concepts Part 1 (Labrosse section p 45: Real-Time Systems Concepts)
  Foreground/Background Systems
  Shared resources
  Critical sections
  Multitasking
  Tasks
  Context switching
ARM Review
  States and Modes
  Registers
  Assembly language instructions
  Interrupt semantics
Assignment 1 – uDebugger tool

## Slide 5: Current Lecture (L2) Overview
Revisit LDREX, STREX
Embedded Operating System Concepts Part 2 (Labrosse Chapter 2)
  Multitasking OS concepts
    The kernel, Preemptive and non-preemptive kernels, The scheduler, Scheduling algorithms, Task states, Parameters used in scheduling – quantum, priority, Priority inversion
  Real time OS concepts
    Definition, Hard/soft real time, Jitter, OS timer tick, Interrupt latency
Context switching on ARM Cortex (Yiu 10.4, 10.5)
Assignment 2: Context Switch (due in 1 week)

## Slide 6: Assignment Grading Policy
Canvas operates on a points system and does not provide a pass/fail option.
However Canvas provides complete/incomplete, so your submissions will be graded as complete or incomplete with zero (0) points.
You may resubmit any assignment to make it complete, except see below:
Submissions will not be accepted after a solution has been released.
Pass threshold corresponds roughly anything higher than C+.

## Slide 7: Revisit LDREX/STREX
Exclusive memory access (Yiu Section 5.6.2, Table 5.21)
The goal is to accomplish the following exclusive access sequence atomically:
  Get the contents of memory location x
  If contents==0
    Success
    Store 1 in location x
  Else
    Failed (try again or give up)

## Slide 8: Revisit LDREX/STREX
Potential Problems:
After memory location x has been read and before it has been written with value 1:
  An interrupt may occur potentially allowing another thread to access memory location x.
  An interrupt handler may exit potentially allowing another thread to access location x.
  Or another processor or bus master may access location x

## Slide 9: Revisit LDREX/STREX
What LDREX Rt, [Rn] does:
Copies the contents of location [Rn] into Rt
Sets the processor’s Local Exclusive Access Monitor bit to indicate that an exclusive access is in progress.
If a bus level Exclusive Access Monitor bit is present it will also be set.

## Slide 10: Revisit LDREX/STREX
What STREX Rd, Rt, [Rn] does:
Attempts to copy the contents of Rt to memory location [Rn], returns status in Rd (success: Rd==0, failure: Rd==1)
Resets the processor’s Local Exclusive Access Monitor bit.
If a bus level Exclusive Access Monitor bit is present it will also be reset.

## Slide 11: Revisit LDREX/STREX
STREX fails if:
The bus level exclusive access monitor (if present) returns an exclusive fail response.
The local exclusive access monitor is not set which can happen if:
  Incorrect exclusive access sequence (LDREX wasn’t executed first)
  An interrupt entry or exit occurred since LDREX was executed
  Execution of a CLREX occurred which clears the local exclusive access monitor.

## Slide 12: Embedded operating system concepts
The Kernel
The part of a multitasking OS responsible for task management
Schedules tasks – does context switching
Provides task synchronization services like semaphores, task communication services like mailboxes and queues (more on that later), task bookkeeping, etc.
Requires CPU time to perform its functions but considered a good trade off for the gain in system manageability
Well designed kernel uses 2-5% of CPU time leaving 95-98% of CPU time for application tasks

## Slide 13: Embedded operating system concepts
Two kernel types
Non-preemptive
  Tasks complete their steps before surrendering the CPU to another task
Preemptive
  the kernel may for various reasons preempt one task before it has completed its steps to allow another task to have control of the CPU

## Slide 14: Embedded operating system concepts
Non-preemptive kernels
A simple approach often sufficient for simple embedded systems running on limited hardware
Similar to foreground-background systems in that tasks execute in the background and are interrupted by ISRs in the foreground
More flexible than foreground-background systems in that tasks don’t have to execute in the same order every time through the super loop
The kernel can change the priority of tasks dynamically in an ISR so that the highest priority task runs next – but it still waits till the current task is done
The current task is never preempted even if a higher priority task is next – it only relinquishes the CPU when it has finished its steps
Consequently, response time is non-deterministic

## Slide 15: Embedded operating system concepts
Preemptive kernels
This type of kernel can preempt a task and switch context to another task even if the first task is not ready to relinquish the CPU
In priority based scheduling a higher priority task that is ready to run should always preempt a lower priority task immediately
Therefore execution of the highest priority task in the system is deterministic

## Slide 16: Embedded operating system concepts
The Scheduler
That part of the kernel that has the job of selecting the next task to run
Various algorithms optimize for different scheduling goals
All scheduling algorithms seek
  Fairness – each task gets its fair share of CPU – no CPU “starvation”
  “Fair” depends on the context and goals – e.g. priority based schemes need to account for varying task priority levels – higher priority tasks must have precedence over lower
  Being fair is easier without priorities however real time constraints may not get met
  Policy enforcement – need to be clear on the policies
  Balance – keeping all parts of the system busy

## Slide 17: Embedded operating system concepts
Scheduling algorithms
Batch scheduling – example: processing big data
  Throughput – maximize jobs per hour
  Turnaround time – minimize time between submission and completion
  CPU utilization – keep the CPU busy all the time
Interactive scheduling – example: web server
  Response time – respond to requests quickly
  Proportionality – meet users’ expectations/perceptions of how long a job “should” take
Real time – example: streaming media – MP3 player
  Meet deadlines
  Predictability - deterministic

## Slide 18: Embedded operating system concepts
Task states
Simplest preemptive kernel has 3 task states – Running, Ready, Blocked
Running - only 1 task at a time is in this state (on a single-core system) and it has control of the CPU
Blocked – tasks in this state are not currently capable of running – e.g. waiting for a shared resource to become available
Ready state – tasks in this state are currently capable of running, just waiting for control of the CPU

## Slide 19: Embedded operating system concepts
MicroC/OS-II terminology note on Task states
uCOS textbook calls the “Blocked” state the “Waiting” state
Could be confusing: both Ready and Blocked tasks are “waiting” but for different things
Blocked tasks are waiting for something to make them capable of running
Ready tasks are capable of running and are just waiting to be assigned control of the CPU
Waiting

## Slide 20: Embedded operating system concepts
Some reasons for state transitions
Ready  Running
  Task gets its “turn” for control of CPU
Running  Ready
  Task’s “time slice” expires
  Task currently has no work to do and “yields” the CPU
  Task is preempted by a higher priority task

## Slide 21: Embedded operating system concepts
Some reasons for state transitions
Running  Blocked
  Task attempts to enter a critical section currently occupied by another task
  Task chooses to delay itself
Blocked  Running
  A task exits a critical section allowing a top priority task to enter the CS
  The blocked task is in a “priority inversion” situation which requires it to be unblocked and run (more on that later)

## Slide 22: Embedded operating system concepts
Some reasons for state transitions
Ready  Blocked
  Another task such as a shell suspends the task, e.g. Linux “suspend” command
Blocked  Ready
    One task exits a critical section which unblocks a waiting task which if it is not top priority will become ready
    A task’s self imposed delay expires

## Slide 23: Embedded operating system concepts
Parameters used in scheduling
Quantum – or time slice
  Round Robin Scheduling:
    Each task gets to control the CPU for a predetermined time period or quantum before the scheduler assigns the CPU to the next ready task
  Too short quantum
    results in frequent context switches
    Context switches are time consuming so can result in too high a percentage of CPU time spent on unproductive work
  Too long quantum
    Tasks can get a lot done in their quantum but
    Tasks may miss deadlines if they have to wait too long for their turn

## Slide 24: Embedded operating system concepts
Parameters used in scheduling
Priority
  With “pure” priority scheduling, the highest priority ready task always gets immediate control of the CPU
  Requires that hi-pri tasks get blocked or self-delay to allow lower priority tasks to run
  Otherwise the globally highest priority task will run 100% of the time
  Pure priority scheduling can result in priority inversion …

## Slide 25: Embedded operating system concepts
Priority inversion
Occurs when a higher priority task ends up blocked indirectly by a lower priority task
Minimum conditions required:
  Represent a task as an ordered pair:
  (name, priority)
  3 tasks (A,1), (B,2), (C,3)
  Priority 1 > 2 > 3
  1 shared resource: R
A priority inversion sequence:
  (C,3) is running and acquires R
  (A,1) preempts (C,3), then blocks waiting for R held by (C,3) (this is not yet priority inversion)
  (B,2) becomes the highest priority ready task and therefore resumes executing
  We now have priority inversion:
  Usually OK: (B,2) prevents (C,3) from running
  Not OK this time: By preventing (C,3) from running, (B,2) indirectly prevents (A,1) from running

## Slide 26: Embedded operating system concepts
Priority inversion
Time --> | t0 | t1 | t2 | t3 | t4 | t5
Task A, pri=1 | blocked | blocked | unblocked by some event | running, try to acquire R | blocked waiting for R | blocked waiting for R
Task B, pri=2 | blocked | blocked | unblocked by some event | ready | running: priority inversion | running: priority inversion
Task C, pri=3 | running | acquire R | ready | ready | ready | ready
Resource R | available | owner=C | owner=C | owner=C | owner=C | owner=C

## Slide 27: Embedded operating system concepts
Priority inversion solution
Priority inheritance
When (A,1) attempts to acquire resource R held by (C,3), the priority of (C,3) is temporarily boosted to higher than (A,1)
Now the sequence becomes:
  (C,3) is running and acquires resource R
  (A,1) preempts (C,3), then blocks waiting for R held by (C,3) however C’s priority is temporarily raised higher than (A,1) thus (C,3 0)
  (B,2) is no longer the highest priority ready task therefore (C,0) continues to run until it releases resource R whereupon its priority is reduced back to 3 (C,0  3)
  When R becomes available, (A,1) is unblocked and resumes since it is the highest priority ready task.

## Slide 28: Embedded operating system concepts
Priority inversion avoidance via priority inheritance
Time --> | t0 | t1 | t2 | t3 | t4 | t5
Task A, pri=1 | blocked | blocked | unblocked by some event | running, try to acquire R | blocked waiting for R | blocked waiting for R
Task B, pri=2 | blocked | blocked | unblocked by some event | ready | running: priority inversion | running: priority inversion
Task C, pri=3 | running | acquire R | ready | ready | ready | ready
Resource R | available | owner=C | owner=C | owner=C | owner=C | owner=C
Time --> | t0 | t1 | t2 | t3 | t4 | t5
Task A, pri=1 | blocked | blocked | unblocked by some event | running, try to acquire R | blocked waiting for R | running, acquire R
Task B, pri=2 | blocked | blocked | unblocked by some event | ready | ready | ready
Task C, pri=3 | running | acquire R | ready | ready, pri=0 | running, release R, pri=3 | ready
Resource R | available | owner=C | owner=C | owner=C | owner=C | owner=A
Priority inversion

## Slide 29: Embedded operating system concepts
Scheduling with a blend of quantum and priority
  Pure Round Robin – no priorities – just use time slices
  Priority tiers - at start of a new quantum, current highest priority runs, else Round Robin for equal priority tasks (priority tiers)
  Non-preemption with priority - at start of new quantum, current highest priority runs, but no preemption till end of quantum even if higher priority task becomes ready during the quantum (via ISR)
  Pure priority scheduling – highest priority always runs, period.

## Slide 30: Embedded operating system concepts
Real-Time OSes
Definition: An RTOS is an operating system intended to serve real-time applications that process data as it comes in, typically without buffering delays. Processing time requirements (including any OS delay) are measured in tenths of seconds or shorter. (Wikipedia)
Hard real-time OS: meets deadlines deterministically – guaranteed response times – must determine worst case performance
Soft real-time OS: can usually or generally meet deadlines – extreme delays are occasionally possible but are considered acceptable

## Slide 31: Embedded operating system concepts
Real-Time OSes
Jitter: the variability in time taken to accept and process a given unit of work – inherent in all digital systems. Worst case jitter delays have to meet real time specifications of the application.
The OS timer tick:
  The “heartbeat” of the OS
  OS bookkeeping is updated – CPU, memory usage per task, etc.
  Update the state of tasks that are waiting for events
  Call scheduler to determine which task should be the “current” task
  Turn control of CPU over to current task

## Slide 32: Embedded operating system concepts
Example: timer jitter
Tick interrupt frequency, say 1 kHz
If we make a 3 msec timer using ticks from this clock there will be an error between 0 and 1 msec depending on where in the tick interval we start counting ticks.
To keep the relative error small, either time larger intervals (say > 1 sec) or use a higher frequency clock.
error

## Slide 33: Embedded operating system concepts
Real-Time OSes
Interrupt latency
Latency for a particular interrupt depends on (quoting Simon)
  The longest period of time during which that interrupt (or all interrupts) are disabled.
  The time it takes to execute any interrupt routines for interrupts that are of higher priority than the one in question.
  How long it takes the processor to stop what it is doing, do the necessary bookkeeping, and start executing instructions within the interrupt routine.
  How long it takes the interrupt routine to save the context and then do enough work that what it has accomplished counts as a “response”

## Slide 34: Embedded Operating System Concepts
Summary
Multitasking OS concepts
  The kernel
  Preemptive and non-preemptive kernels
  The scheduler, Scheduling algorithms
  Task states
  Parameters used in scheduling – quantum, priority
  Priority inversion
Real time OS concepts
  Definition
  Hard/soft real time
  Jitter
  OS timer tick
  Interrupt latency

## Slide 35
“Don’t just do something – sit there!”
Jean Labrosse
Break
Quiz
After the break
Revisit Assignment 1
Context switch

## Slide 36: Context switching on Cortex-M4

## Slide 37: Context switching (Assignment 2)
Let’s look at a basic context switch scenario:
  2 tasks: taskOne, taskTwo
  Timer tick interrupt occurs every 200 msec
  On each tick,
    Save the context of the current task in its own stack
    Call a simple scheduler that will select the other task and make it the current task
    Restore the context of the current task from its stack
    Resume executing the current task
  Tasks will run in Thread Mode, use Main SP, privileged level
  Timer tick interrupt occurs in Handler mode, uses Main SP, privileged level (as do all interrupts)

## Slide 38: Context switch flow diagram
Current Task:
Only one task at a time can run.
This is the current task.

## Slide 39: Code for tasks to execute
// taskOne counts up from 0.
// Never exits.
//
void taskOne(void)
{
int count = 0;
while(1)
{
printString("task one: ");
print_uint32(count++);
printString("\n");
int i;
for(i=0;i<10000;i++); // delay
}
}
// taskTwo counts down from 0xFFFFFFFF
// Never exits.
//
void taskTwo(void)
{
int count = 0xFFFFFFFF;
while(1)
{
printString("task two: ");
print_uint32(count--);
printString("\n");
int i;
for(i=0;i<10000;i++); // delay
}
}

## Slide 40: One stack per task
// Default size of stacks.
#define STACKSIZE 256
// Allocate space for two stacks
int stackOne[STACKSIZE];
int stackTwo[STACKSIZE];
int stackOneSP; // Value of task 1's stack pointer
int stackTwoSP; // Value of task 2's stack pointer

## Slide 41: Key variables in Context Switch Homework
taskID: an integer, either 1 or 2 indicating the current task ID.
stackOneSP: 32-bit word to store the SP register value for taskOne when it is switched out (not running)
stackTwoSP: 32-bit word to store the SP register value for taskTwo when it is switched out (not running)
currentSP: 32-bit word which gets set to one of the above values by the Scheduler when switching to a new context.

## Slide 42: PendSV – a special Cortex-M4 exception
PendSV is a special Cortex-M exception intended for context switching
Always triggered explicitly by software (in SysTick_Handler)
Convention requires that PendSV priority be set to lowest value (0xFF)
The reason a context switch should have lowest priority is that it should never happen while any interrupt other than PendSV is being handled
In other words, all other interrupts must finish being serviced before a context switch can take place

## Slide 43
43
43
43
Context switch trace (Cortex-M4)
43
Registers
SRAM
stack
stackOne
stack
stackTwo
task
code
taskOne
task
code
taskTwo
R0 | 
R1 | 
R2 | 
R3 | 
R4 | 
R5 | 
R6 | 
R7 | 
R8 | 
R9 | 
R10 | 
R11 | 
R12 | 
MSP | 
LR | 
PC | 
xPSR | 
PRIMASK | 00000000
stackOneSP
currentSP
stackTwoSP
handler
code
TaskSwitch
Copy to
Points to
1 taskOne is current and running
In Thread mode
MSP points somewhere in stackOne
PC points somewhere in taskOne code
PRIMASK is 0 (interrupts enabled)
stackTwoSP points to saved context of taskTwo
Flash Memory

## Slide 44
44
44
44
Context switch trace (Cortex-M4)
44
Registers
SRAM
stack
stackOne
stack
stackTwo
task
code
taskOne
task
code
taskTwo
R0 | 
R1 | 
R2 | 
R3 | 
R4 | 
R5 | 
R6 | 
R7 | 
R8 | 
R9 | 
R10 | 
R11 | 
R12 | 
MSP | 
LR | 
PC | 
xPSR | 
PRIMASK | 00000000
stackOneSP
currentSP
stackTwoSP
handler code
TaskSwitch
Copy to
Points to
2 Timer tick occurs
R0-R3, R12, LR, PC, xPSR are stacked by NVIC
SysTick_Handler triggers a PendSV interrupt and returns
PendSV immediately enters TaskSwitch, “re-using” the stack frame already saved for the timer interrupt (“tail-chaining”)
Flash Memory

## Slide 45
45
45
45
Context switch trace (Cortex-M4)
45
Registers
SRAM
stack
stackOne
stack
stackTwo
task
code
taskOne
task
code
taskTwo
R0 | 
R1 | 
R2 | 
R3 | 
R4 | 
R5 | 
R6 | 
R7 | 
R8 | 
R9 | 
R10 | 
R11 | 
R12 | 
MSP | 
LR | 
PC | 
xPSR | 
PRIMASK | 00000001
stackOneSP
currentSP
stackTwoSP
handler code
TaskSwitch
Copy to
Points to
3 Save remaining context
Disable interrupts with CPSID I (PRIMASK = 1)
R4-R11 are stacked by TaskSwitch handler
MSP points to saved context of taskOne
MSP is saved to currentSP
Flash Memory
1
2

## Slide 46: Contents of saved context in stackOne
R13 (MSP) is not saved in the stack – we save it to currentSP
Next step is to call scheduler to select next task
Stack bottom (higher address)
Stack top (lower address)
xPSR
PC
LR
R12
R3
R2
R1
R0
R11
R10
R9
R8
R7
R6
R5
R4
Stacked by
hardware
Stacked by ISR

## Slide 47
47
47
47
Context switch trace (Cortex-M4)
47
Registers
SRAM
stack
stackOne
stack
stackTwo
task
code
taskOne
task
code
taskTwo
R0 | 
R1 | 
R2 | 
R3 | 
R4 | 
R5 | 
R6 | 
R7 | 
R8 | 
R9 | 
R10 | 
R11 | 
R12 | 
MSP | 
LR | 
PC | 
xPSR | 
PRIMASK | 00000001
stackOneSP
currentSP
stackTwoSP
handler code
TaskSwitch
Copy to
Points to
4 Call the scheduler
scheduler() gets called from TaskSwitch handler
scheduler() is written in C
Saves currentSP in stackOneSP
stackOneSP now points to saved context of taskOne
Copies stackTwoSP to currentSP
Flash Memory
1
2

## Slide 48
48
48
48
Context switch trace (Cortex-M4)
48
Registers
SRAM
stack
stackOne
stack
stackTwo
task
code
taskOne
task
code
taskTwo
R0 | 
R1 | 
R2 | 
R3 | 
R4 | 
R5 | 
R6 | 
R7 | 
R8 | 
R9 | 
R10 | 
R11 | 
R12 | 
MSP | 
LR | 
PC | 
xPSR | 
PRIMASK | 00000000
stackOneSP
currentSP
stackTwoSP
handler code
TaskSwitch
Copy to
Points to
5 Resume current task (taskTwo)
Copy currentSP to MSP
MSP now points to saved context of taskTwo
Restore R4-R11 using MSP
Enable interrupts by setting PRIMASK=0
Execute a return from interrupt which will restore R0-R3, R12, LR, PC, xPSR from stackTwo
Flash Memory
1
2

## Slide 49
49
49
49
Context switch trace (Cortex-M4)
49
Registers
SRAM
stack
stackOne
stack
stackTwo
task
code
taskOne
task
code
taskTwo
R0 | 
R1 | 
R2 | 
R3 | 
R4 | 
R5 | 
R6 | 
R7 | 
R8 | 
R9 | 
R10 | 
R11 | 
R12 | 
MSP | 
LR | 
PC | 
xPSR | 
PRIMASK | 00000000
stackOneSP
currentSP
stackTwoSP
handler code
TaskSwitch
Copy to
Points to
6 taskTwo is current and running
In Thread mode
MSP points somewhere in stackTwo
PC points somewhere in taskTwo code
PRIMASK is 0 (interrupts enabled)
stackOneSP points to saved context of taskOne
Flash Memory

## Slide 50: scheduler
void scheduler(uint32_t sp)
{
if (taskID == 1) {
stackOneSP = sp; // Store stack pointer for task 1
taskID = 2; // Set the taskID to task 2
currentSP = stackTwoSP; // Set the current stack pointer
// to task 2's stack pointer
} else {
stackTwoSP = sp; // Store stack pointer for task 2
taskID = 1; // Set the taskID to task 1
currentSP = stackOneSP; // Set the current stack pointer
// to task 1's stack pointer
}
}

## Slide 51: Initializing our multitasking system
Ensure that PendSV priority is set to lowest
Need to set up the initial context for a task on its stack
  xPSR initial value is 0x01000000 i.e. bit 24 indicates Thumb mode.
  PC is next and gets set to the entry point of the task code
  LR doesn’t matter because the task should never return
  All the other registers can have any values we choose
Set taskID to 1
Start multitasking by explicitly calling taskOne()
taskOne will execute until timer tick triggers PendSV which invokes ContextSwitch.
ContextSwitch will switch control to the initial context of taskTwo
Notes: CORRECTION:
  Last thing to push is cpsr to ensure mode is SVC
Corrected to
  Last thing to push is cpsr to ensure mode is SVC and interrupts are enabled

## Slide 52: Stack initialization
*(--stkptr) = 0x01000000uL; // xPSR
*(--stkptr) =
(uint32_t)task_address; // Entry Point
// of task code
*(--stkptr) = 0x14141414uL; // R14 (LR)
*(--stkptr) = 0x12121212uL; // R12
*(--stkptr) = 0x03030303uL; // R3
*(--stkptr) = 0x02020202uL; // R2
*(--stkptr) = 0x01010101uL; // R1
*(--stkptr) = 0x00000000uL; // R0
*(--stkptr) = 0x11111111uL; // R11
*(--stkptr) = 0x10101010uL; // R10
*(--stkptr) = 0x09090909uL; // R9
*(--stkptr) = 0x08080808uL; // R8
*(--stkptr) = 0x07070707uL; // R7
*(--stkptr) = 0x06060606uL; // R6
*(--stkptr) = 0x05050505uL; // R5
*(--stkptr) = 0x04040404uL; // R4
Notes: CORRECTION:
  Last thing to push is cpsr to ensure mode is SVC
Corrected to
  Last thing to push is cpsr to ensure mode is SVC and interrupts are enabled

## Slide 53: Explore Assignment 2 in the debugger
Download ContextSwitch.zip, unzip, load the workspace in EWARM
Things to notice in main.c:
  stackOne, stackTwo, taskOne(), taskTwo(), scheduler()
  Multitasking kickoff steps in main()
Things to notice in stack.c:
  Only the xPSR and PC values are important. The rest of the registers values don’t really matter
Things to notice in hw_init.c:
  Configure SysTick to interrupt every 200 msec
  Configure PendSV interrupt priority to lowest
Things to notice in startup.s:
  PendSV handler set to TaskSwitch
Things to notice in interrupt.c:
  Trigger PendSV exception in SysTick_Handler()
Things to notice in switch.s:
  This is where you need to add code to perform the context switch
Notes: CORRECTION:
  Last thing to push is cpsr to ensure mode is SVC
Corrected to
  Last thing to push is cpsr to ensure mode is SVC and interrupts are enabled

## Slide 54: Explore Assignment 2 in the debugger
Startup TeraTerm
Build, upload and run the project
Break into the program and notice that the TeraTerm output consists of output from the loop in taskOne()
This is expected since TaskSwitch has not been implemented
Resume running the program
Set breakpoints and observe register values:
  Breakpoint in taskOne()
  Breakpoint in TaskSwitch
Notes: CORRECTION:
  Last thing to push is cpsr to ensure mode is SVC
Corrected to
  Last thing to push is cpsr to ensure mode is SVC and interrupts are enabled

## Slide 55: Explore Assignment 2 in the debugger
We’ll then look at the output with the context switch implemented
Notice we now get output from both taskOne and taskTwo
Notice some loss of data due to shared buffer not protected by critical section
Breakpoints in
  taskOne()
  taskTwo()
Notes: CORRECTION:
  Last thing to push is cpsr to ensure mode is SVC
Corrected to
  Last thing to push is cpsr to ensure mode is SVC and interrupts are enabled